## Slide 1: Modeling Soil and Hydrologic Processes
Presented by Ryan Boylan
REACCH Teachers Workshop
Summer 2013

## Slide 2: Overview
Model: What, why and types
History of soil erosion modeling
Process based models: WEPP
Hydrologic Characterization Tool
  where to find it and how to use it.

## Slide 3: What is a Model?
A human construct that helps us better understand physical process in real world systems.
http://www.soilmonoliths.org/
http://www.cs.toronto.edu/~sme/PMU199-climate-computing/pmu199-2012F/Globe_as_a_grid.jpg
Notes: General Circulation models
Global climate modles

## Slide 4: Why use a Model?
Policy decisions
Management decisions
Understanding complex systems
Predicting future scenarios
Education
Hypothesis testing

## Slide 5: How do you use models?
In the classroom

## Slide 6: Types of Models
Physical:
Notes: James Watson and Francis Crick

## Slide 7: Types of Models
Mathematical: statistical
http://www.earthsurfacehydrology.nl/wp-content/uploads/2012/01/Syllabus_Stochastic-Hydrology.pdf

## Slide 8: Types of Models
Empirical: Derived from experimental data
Universal Soil Loss Equation (USLE):
A=RKLSCP
  A = predicted soil loss
  R = Rainfall and runoff
  K = Soil Erodibility
  L = Slope length
  S = Slope gradient or steepness
  C = Cover and management
  P = Erosion control practice

## Slide 9: K factor Soil Erodibility Mathematical Model

## Slide 10: Types of Models
Conceptual: Visualization

## Slide 11: Types of Models
Process based:
Notes: These models try to represent the physical processes observed in the real world.
Measureable parameters.
Driven by the principles of physics

## Slide 12: Simple vs. Complex
“For every complex question there is a simple and wrong solution." A. Einstein.
Data
Simple
Complex
Model Complexity

## Slide 13: History of Soil Erosion Modeling

## Slide 14: History of Soil Erosion Modeling
Congress funds $160,000 in 1929
Sets up 10 experimental stations, Pullman, WA
New Deal = Soil Erosion Services 1933
http://rock.rapgenius.com/Mumford-and-sons-dustbowl-dance-lyrics
Notes: Hugh Hammond Bennett Pushed for funding from congress
The National Industrial Recovery Act was part of Roosevelt’s "New Deal" program, and it established the Soil Erosion Service (SES) under the Department of the Interior in 1933,
Bennett headed the new agency, and also utilized workers from the Civilian Conservation Corps (CCC) to build drop inlets, grass waterways, fix gullies, and plant trees to control erosion.

## Slide 15: History of Soil Erosion Modeling
SES ->ARS
10,000 plot years of data analyzed 1933-1953
Universal Soil Loss Equation (USLE)
RUSLE, RUSLE2
Watershed Erosion Prediction Project (WEPP), 1985
http://www.ars.usda.gov/Research/docs.htm?docid=18093
Notes: National Runoff and Soil Loss Data Center was created at Purdue University under the direction of Walt Wischmeier. At Perdue university
By the end of 1937, 23 states had district laws and by 1947 all states had soil and water district laws and over 1300 Soil and Water Conservation Districts (Swedes) had been established to assist farmers and landowners in controlling erosion problems

## Slide 16: What is Erosion
Detachment, transport and deposition of soil particles water.

## Slide 17: Erosion is complex
Climate
Pullman, WA
Moscow, ID
Notes: Rainfall & Wind both play a role in erodibility. The image shows rainfall across the region. General trends show increased rainfall as one moves east.

## Slide 18: Erosion is complex
Climate
Soils
Notes: Soil type plays an important role in determining erodibility. The legend is included not to read the individual soil types, but to show the large number of soil types represented in the region.

## Slide 19: Erosion is complex
Climate
Soils
Vegetation
Notes: Ground cover includes living and decomposing organic matter.

## Slide 20: Erosion is complex
Climate
Soils
Vegetation
Topography
Geology

## Slide 21: Watershed Erosion Prediction Project (WEPP)
Models soil erosion processes by water
Hillslope model
Was developed cooperatively with 1985:
  ARS, NRCS (SCS), BLM, Forest Service
1991: First stable release
1995: Rewritten code and Watershed release
Notes: An erosion modeling application.

## Slide 22: WEPP Windows – Hillslope (1999)
Notes: This is a screen shot from a computerized erosion model. The lab activity for this unit uses a different model.

## Slide 23: WEPP Processes 1
Rainfall, snowmelt, infiltration, subsurface lateral flow, percolation, runoff, soil water

## Slide 24: WEPP Processes 2
Soil detachment, transport, deposition and delivery

## Slide 25: WEPP Processes 3
Plant growth, evapotranspiration, and senescence

## Slide 26: WEPP Processes 4
Residue accumulation and decay

## Slide 27: WEPP Processes 5
Soil consolidation

## Slide 28: Erosion Processes 1
Interrill or sheet erosion
  Raindrop splash
  Shallow Overland Flow

## Slide 29: Erosion Processes 2
Rill Erosion
  Concentrated Channel Flow

## Slide 30: Erosion Processes 3
Interrill Erosion
  Raindrop splash
  Shallow Overland Flow
Rill Erosion
  Concentrated Channel Flow
WEPP does NOT model gullying or landslides

## Slide 31: Overland Flow Elements
Describe variation in soil and vegetation down a hillslope
OFE 1
OFE 2
OFE 3
Notes: This is how this model predicts erosion from a slope.

## Slide 32: WEPP Water Balance
Percolation
Lateral
Flow out
Surface runoff
Percolation
perched
layer
ET
P
Surface runoff
Lateral
Flow in
Notes: ET-Evapotranspiration, P-precipitation,

## Slide 33: WEPP Outputs
Summaries
  Average Annual, Annual, monthly, or event:
Graphics
  Erosion distribution along a hillslope
  And a whole lot of other stuff

## Slide 34: WEPP Outputs
Text
  Combinations of daily parameter values

## Slide 35: Simplifications
WEPP is too complex!
  Simplify input files to a few key parameters
WEPP takes too long to set up!
  Break up watershed into “characteristic” land types
How reliable are the predictions?
  More concerned with general trends rather than direct comparison

## Slide 36: Current Needs
Better tools are needed to identify critical areas in a watershed and improve them with appropriate Best Management Practices (BMP). (Mulla et al., 2008)
  Simple
  Minimal data requirements
  Minimal calibration

## Slide 37: Watershed
Pollutant
Hydrologic Active Areas
Hydrologic Sensitive Areas (HSAs)
Targeted Management to reduce
pollutant loading at the least cost
Walter et al. (2001)
Time and space

## Slide 38: CEAP Watersheds
Notes: 13 watersheds in the United States
Conservation effects assessment project

## Slide 39: Hydrologic Characterization Tool (HCT)
Notes: The simplified version of WEPP, free and online

## Slide 40: Hydrologic Characterization Tool
Site-specific:
    Local climate, soils, topography, crop rotation, management
Simulates major flow paths
    Infiltration, runoff, subsurface lateral flow, percolation
Spatial Scale
    Characteristic land types
Temporal Scale
    Daily to Monthly
Flexible
    Incorporate local knowledge

## Slide 41
Notes: Screenshots

## Slide 42: Output

## Slide 43: Output

## Slide 44: Output

## Slide 45: Where to find HCT
http://wepp.ag.uidaho.edu/cgi-bin/HCT.pl
Or simply Google:
Hydrologic Characterization Tool

## Slide 46: A note to end on:
"All models are wrong but some are useful" George E.P. Box

## Slide 47: How can this be used in the class room?
Great follow-up to the Erosion and Infiltration lab.
Simple to use and student friendly computer model

## Slide 48: Modeling Activity:
Double Click to open Word Doc